## Slide 1: Weekly Meeting
Jon Earle

## Slide 2: Settings
Node-count intervals: 5, 7, 10, 12, 14, 17, 22, 32, 52, 77, 102
Simulations per interval: 20
Number of intervals: 11
Total simulations: 220
Simulation duration: 30 minutes
Random seed: 44

## Slide 3: Settings
Region: US
Channel number: 27
Operating frequency: 908.750 MHz
Transmit power: 20 dBm
Regional power limit: 30 dBm
Antenna gain: 2 dBi
Antenna height: 1.0 m
Modem preset: LONG_FAST
Bandwidth: 250 kHz
Spreading factor: 11
Coding rate: 4/5
Receiver sensitivity: -131.5 dBm
CAD threshold: -134.5 dBm
Preamble length: 16 symbols
Payload length: 40 bytes
Header length: 16 bytes
ACK length: 2 bytes
Noise level: -119.25 dB

## Slide 4: Settings
Routing algorithm: MANAGED_FLOOD
Node role: CLIENT
Router mode: False
Hop limit: 3
Maximum retransmissions: 3
Traffic type: Broadcast
Direct messages enabled: False
Mean message interval: 100 seconds
Message-generation distribution: Exponential

## Slide 5: Settings
Path-loss model number: 6
Path-loss model name: 3GPP metropolitan macro-cell
Gamma: 2.08
Reference distance: 40.0 m
Path loss at reference distance: 127.41 dB
Asymmetric links enabled: True
Asymmetric-link mean offset: 0 dB
Asymmetric-link standard deviation: 2 dB